## Slide 1
3- System Architecture

## Slide 2
OEM Website
Apply Security Bot
Store Cipher File and Digest in Firebase
Server Side
Cloud Server
Organize Hex File
Notify Telematic Unit
Check Authentication
Firebase
Telematic Unit
Check Security Principles
Send and Receive User Reply
Parse and Send Hex File
Esp32
Gateway Unit
Check Safe Mode
Deliver Hex File to Correct Target
Stm32f103
UI Unit
Show Update Message
Touch Screen
Target ECU
Receive Hex File
Flash Update Using Bootloader
Stm32f103
Receive and Send User Reply
Raspberry Pi 3 Model B
Tx
Rx
CANH
CANL
HTTP
HTTP
HW Module:
Hardware
Architecture
Upload Hex File
Client Side
HDMI
Target ECU
Receive Hex File
Flash Update Using Bootloader
Stm32f103

## Slide 3
HTTP
HTTP
Tx
Rx
CANH
CANL
HDMI
Hardware
Architecture

## Slide 4
Hardware Specs
• Operating at 72 MHz frequency
• Flash memory up to 128 Kbytes
• It offers two 12-bit ADCs
• 3 general-purpose 16-bit timers
• 2x I2Cs.
• 2x SPIs
• 3x USART
• 1x USB
• 1x CAN
Microcontroller Dual Core ,operating at 240 MHz
The SRAM 520 KB
Flash memory: 4 MB
Built-in secure wi-fi module 802.11 BGN HT40
30 GPIO leads, including:
  3x UART
  3x SPI
  2x I2C (2x I2S)
Supports 1 Mb/s operation
High noise immunity due to differential bus Implementation
Up to 112 nodes can be connected
Low current standby operation
Stm32f103
Esp32
Mcp 2551

## Slide 5
Hardware Specs
Raspberry Pi 3 Model B
7inch Capacitive Touch Screen
• Operating at 1.2 GHz frequency.
• Broadcom VideoCore IV operates at 250MHz.
• 4 USB 2.0 ports.
• Audio output Analog via 3.5 mm phone jack.
• Digital audio signals via HDMI.
• 1GB Kbytes of SDRAM.
• 17x GPIO that can be used as:
• I2C.
• SPI.
• USART.
• I2S audio.
size 7inch
Resolution1024×600
Display Interface HDMI / VGA
Touch Type Capacitive
Audio Output 3.5mm Jack

## Slide 6
Architecture
Software
OS
APP
LAYER
SERVICE
LAYER
HAL
LAYER
MCAL
LAYER
APP
LIBRARY
BIT MATH
STD TYPE
RCC
TIMER
CAN
GPIO
USART
EXTI
SPI
SYS-TICK
DMA
FBEC
NVIC
AFIO
SPEED
SCREEN
Wi-Fi
Motors

## Slide 7
Cloud Server

## Slide 8
OEM Website
Express.js
Node.js
MongoDB
Server Side
Cloud Server
Storage
Real Time Database
Authentication
Firebase
HTTP
HTML
CSS
JavaScript
Client Side
Cloud Server

## Slide 9
FIREBASE SERVICES
Firebase is a Google-backend Web app development based on the backend as a service system.
It has the ability to manage data in real-time and provides an enhanced app-usage experience to the users.
We interested in firebase database and firebase authentication

## Slide 10
FIREBASE SERVICES
Authentication
Realtime Database
Storage

## Slide 11
FIREBASE SERVICES
All Modules for each Brand
All Brands
ALL Years for each Module
Update files for each Year

## Slide 12
FIREBASE SERVICES
Realtime Database Flags

## Slide 13
Telematic unit

## Slide 14
OEM Website
Express.js
Node.js
MongoDB
Server Side
Cloud Server
Storage
Real Time Database
Authentication
Firebase
Telematic Unit
32-bit LX6 Microprocessor
up to 240 MHz
802.11,up to 150Mbps
520 KB of SRAM
448 KB of ROM
Esp32
Tx
Rx
HTTP
HTTP
HTML
CSS
JavaScript
Client Side
Telematic Unit

## Slide 15
Telematic Unit
Using ESP32 as a Telematic Unit to do four process :
Using WIFI Module to Connect with Firebase to :
Check if we have new update
take a New update and store it in system file memory section
Check Security Principles
Confidentiality
Authentication
Integrity
Notify HMI about new Update
Parsing Hex File and using UART to send Record by Record

## Slide 16
Telematic Unit
Connect WiFi
sign in to Firebase
check User Reply
Download Hex file to ESP32 Memory
Parsing HEX File
Check Realtime Database
send notification to HMI
True
False
Wait Ack from STM
Send Record
File Free?
Write False In Realtime Database
Repeat ESP32 Authentication
YES
NO
Accept
Store notification in HMI
Wait Accept Reply
Wait
OK
NOK

## Slide 17
Telematic Unit

## Slide 18
Telematic Unit
No Update Available
Update Available ,and Wait Reply

## Slide 19
Telematic Unit
Used Accepted Update , Send All Record and Change Realtime Database To false